## Slide 1
Shunyang Li | Public technical brief | October 2026
8× RTX PRO 5000 · vLLM-Omni
Real-Time Video Generation With MiniMax H3
Notes: This talk has two parts: taking MiniMax H3 toward real-time generation on eight RTX PRO 5000 GPUs, then using vLLM-Omni as the multi-GPU backend for ComfyUI applications.

## Slide 2
01 Toward Real-Time H3 Generation
02 vLLM-Omni and ComfyUI Applications
Notes: Part one covers the real-time target, platform constraints, bottleneck analysis, distributed optimization, and validation. Part two uses the public ComfyUI integration and PR #9194 workflows as the application story.

## Slide 3
01 · Real-Time H3 Generation
Notes: Part one moves from the real-time definition to the eight-GPU baseline, bottleneck analysis, optimization, and validation.

## Slide 4: Real-Time Ref2VA Raises the Systems Bar
A 124-frame clip at 24 FPS is real time only when end-to-end latency stays below 5.167 s (RTF < 1)
RTF = latency ÷ media duration; the 124-frame deadline is 5.167 s. H3 has the largest dense backbone in this peer set; Wan2.2 has 27B total and 14B active parameters
Generative Backbone · Full Parameters (B)
32B encoder → 33B dense Omni Transformer → visual/audio VAE. Fifty blocks × 50 steps keep compute and memory pressure high; about 13B AdaLN parameters can be cached
Model Capability · Native 768P · 33B Dense
Chart: 
| MiniMax H3 | Wan2.2 A14B | LTX-2.5 | HunyuanVideo-1.5
Full parameters (B) | 33 | 27 | 22 | 8.3
Notes: Real time is RTF = end-to-end generation latency divided by finished-media duration, with RTF <= 1.0. The baseline is MiniMax H3 Base Ref2VA at 960x544: 124 frames / 24 FPS = 5.167 s. It uses 50 denoising steps, BF16, eight GPUs with USP8, local NCCL, and no RDMA. MiniMax H3 uses a 33B dense Omni Transformer with 50 Transformer blocks; the reference workload runs 50 denoising steps. These are distinct dimensions. Wan2.2 A14B is 27B total / 14B active, LTX-2.5 uses its official 22B designation, and HunyuanVideo-1.5 is 8.3B. The comparison excludes text encoders. Open H3-Base targets native 768p; the H3-Regenerate-2K module is not part of the open release and is excluded. The 130 GB figure is the raw BF16 size of the 32B encoder plus 33B generator, before VAE, activations, attention workspace, and CUDA Graph pools. Sources: https://huggingface.co/MiniMaxAI/MiniMax-H3 ; https://github.com/Wan-Video/Wan2.2 ; https://huggingface.co/Lightricks/LTX-2.5 ; https://github.com/Tencent-Hunyuan/HunyuanVideo-1.5

## Slide 5: SM120 Brings FP4 Compute; PCIe Limits Scale
All discrete SM120 cards pair fifth-generation Tensor Cores with GDDR7 and PCIe Gen5; none provides GPU-to-GPU NVLink
SKU | Compute | Memory | GPU I/O / Fabric
RTX PRO 5000 ×8 Blackwell | SM120 · 110 SMs 5th-gen Tensor · FP4 | 72 GB GDDR7 ECC 48 GB variant | PCIe Gen5 ×16 Planned: NIC → RDMA*
RTX PRO 6000 WS / Server | SM120 · 188 SMs 5th-gen Tensor · FP4 | 96 GB GDDR7 ECC | PCIe Gen5 ×16 No GPU NVLink
GeForce RTX 5090 | SM120 · 170 SMs 5th-gen Tensor · FP4 | 32 GB GDDR7 | PCIe Gen5 ×16 No NVLink
DGX Spark · GB10 | SM121 · 48 SMs 5th-gen Tensor · FP4 | 128 GB unified LPDDR5X | NVLink-C2C in SoC 200 Gb/s ConnectX-7
Notes: The template's native Table Example is reused at its original coordinates with its native table style and typography. RTX PRO 5000, RTX PRO 6000 and GeForce RTX 5090 use compute capability 12.0 / SM120; each has fifth-generation Tensor Cores with FP4 support. DGX Spark's GB10 uses compute capability 12.1 / SM121 and fifth-generation Tensor Cores with FP4 support. The planned RTX PRO 5000 scale-out path is GPU memory to PCIe Gen5 to a compatible NIC and then the RDMA fabric. This path is a deployment plan, not a measured result; GPUDirect RDMA requires compatible software and PCIe topology. The first row marks the selected eight-GPU RTX PRO 5000 baseline. Sources: https://developer.nvidia.com/cuda/gpus ; https://www.nvidia.com/en-gb/products/workstations/professional-desktop-gpus/rtx-pro-5000/ ; https://docs.nvidia.com/cuda/gpudirect-rdma/

## Slide 6: Latency Breakdown
NCCL occupies 49.2% of the mean GPU timeline
Stage | Mean Time per GPU* | Share
Mean GPU timeline* | 250.0 s | 100.0%
NCCL communication | 123.0 s | 49.2%
↳ DiT collectives | 116.1 s | 46.4%
↳ Encoder, VAE, and other collectives | 7.0 s | 2.8%
Tensor compute | 84.5 s | 33.8%
↳ Attention | 45.3 s | 18.1%
↳ GEMM / MLP | 39.2 s | 15.7%
AdaLN weight staging + device layout | 38.5 s | 15.4%
Encoder, VAE, and other GPU work | 4.0 s | 1.6%
  Of 38.5 s/GPU, 36.9 s is AdaLN projection weight staging from CPU; layout is 1.5 s
  This run uses the default runtime cache, not a complete precomputed schedule sidecar
Notes: The measured baseline is MiniMax H3 Base Ref2VA at 960x544, 124 frames, 24 FPS, 50 denoising steps, BF16, and eight RTX PRO 5000 GPUs with USP8. Communication uses local NCCL; RDMA is disabled. The media duration is exactly 124 / 24 = 5.1667 seconds, shown as 5.167 seconds. The four top-level rows are mutually exclusive accounting buckets. The locked endpoint cohort contains three steady requests at 247.956, 246.201 and 248.298 seconds; its median is 247.956 seconds and RTF 47.992. The separately rerun matched Nsight request took 252.773 seconds, or RTF 48.924, after a 253.075-second warmup. Its warmup and measured outputs share one SHA-256 and fully decode. The matched trace reaches 60,827 MiB during the measured request and 61,299 MiB across the sampled run. The table is a hierarchy. NCCL communication includes DiT collectives and collectives in encoder, VAE and other work. It is reported separately from tensor compute and AdaLN host-to-device weight staging/layout. The four top-level cost centers are mutually exclusive and sum to 100 percent. The matched request passed the eight-device, kernel-count, attribution, transport and exclusive-accounting gates, and its CUDA kernel and memory totals match independent nsys stats exactly. The share denominator is kernel, memcpy and memset duration summed across all eight GPUs. The time column divides each category by eight and reports mean operation time per GPU. An interval-union check found no same-GPU overlap among the classified kernel/copy activities, and per-rank activity totals are 247.86 to 248.69 seconds, close to the measured E2E. NCCL kernel duration includes synchronization and peer waiting, so the DiT collective share of 46.4 percent is serialized collective residency rather than pure transfer time or an achieved-bandwidth measurement. The repeated loop issues 10,000 SendRecv kernels per rank: four per DiT block across 50 steps and 50 blocks. DiT host-to-device copies contribute 295.3 aggregate GPU-seconds and 8.94 TB of CUPTI logical bytes. More than 99.998 percent of that H-to-D time comes from staging AdaLN projection BF16 weight and bias on exact-cache misses. The run uses the default 256 MiB runtime output cache and does not configure a complete offline schedule sidecar. Ordinary Attention, MLP and QKV weights remain resident after initialization. This page stops at measured Base50 evidence. Optimization methods begin on the following slides.

## Slide 7: How Denoising Works
State and direction
  x(t) is the current latent; the DiT predicts a data-ward velocity
Solver update
  Euler advances x(t) by a small interval along that velocity
  The next DiT call needs the new latent, so conventional steps run in sequence
Network function evaluation (NFE)
  One NFE is one complete DiT forward
Base H3
  50 NFE × 50 main blocks = 2,500 main-block passes
H3 follows a learned velocity field from noise toward clean video and audio latents
A chain of dependent solver updates turns noise into clean latents
Classical Flow-Matching Sampling
Notes: This page defines the sampling terms used by the rest of the deck. A latent state x(t) is the current compressed video and audio representation. The DiT reads that state, its time coordinate and the prompt or reference conditioning, then predicts a data-ward velocity. The Euler solver uses that velocity to construct the next latent. Conventional sampling is sequential because the next DiT call requires the state produced by the previous update. NFE means network function evaluation; one NFE is one complete DiT forward, not one Transformer block. Base H3 uses 50 sequential NFEs. Each NFE traverses the 50-block main Transformer trunk, so the repeated trunk workload is 50 times 50, or 2,500 main-block passes. Under USP8, each of eight ranks executes its local shard, which is why a system trace can show 20,000 rank-local attention launches. Prompt and reference encoding happen before the repeated loop, and VAE decoding happens after it. H3 uses separate shifted Euler schedules for video and audio; x(t) and delta-t on this page deliberately abstract those two modality-specific updates, which share one joint DiT forward. Sources: https://research.nvidia.com/labs/genair/pdd/ ; https://github.com/MiniMax-AI/MiniMax-H3/blob/main/transformer/config.json

## Slide 8: PDD Turns 50 DiT Passes Into 8
Teacher targets
  Base H3 supplies the mean denoising direction for each fine interval
One student pass
  From the same noisy latent, predict four consecutive directions in parallel
Advance and repeat
  Combine the four predictions to cross one block; repeat from the new latent
H3 PDD8
  Train a new 32-interval grid: 32 ÷ 4 = 8 passes
  Repeated block calls: 2,500 → 400 (−84%)
Predict four denoising directions in parallel; advance one interval block per pass
Paper example: N = 12, L = 4 · H3 PDD8: N = 32, L = 4
N = fine intervals · L = intervals predicted in parallel
Notes: Video generation starts from noise. Base H3 runs the full DiT once for each denoising update, so the model runs 50 times. Parallel Decoding Distillation uses Base H3 as the teacher and trains a student to predict several fine-interval updates in one DiT evaluation. The released H3 Ref2VA PDD adapter uses a new 32-interval schedule and predicts four interval velocities per evaluation, so 32 divided by 4 equals eight DiT evaluations. This is not the same as selecting eight of the original 50 solver steps. Each H3 evaluation still crosses 50 DiT blocks, so repeated block executions fall from 50 times 50, or 2,500, to 8 times 50, or 400. That is 84 percent fewer repeated block calls, reducing repeated attention, GEMM/MLP, and USP communication together. The 84 percent figure is workload arithmetic, not measured end-to-end speedup; encoders, VAE, data movement, memory, and matched quality still require end-to-end validation. NVIDIA Figure 2 shows the generic N=12, L=4 mechanism; the H3 N=32, L=4 schedule is labeled outside the paper figure.

## Slide 9: VSA Makes Attention Sparse
Dense workload
  34,373 tokens → 1.181B pairs/head/block at 544P
Learned VSA route
  Partition → coarse score → Top-K → fine attention → gate
Paper defaults
  4 × 4 × 4 = 64 tokens per cube · Top-K = 32 KV cubes
System boundary
  Attention compute becomes sparse; USP8 still exchanges full-length Q/K/V/O
  Needs sparse-trained routing and gate weights
Video Sparse Attention learns which 3-D video cubes matter
Paper: 64-token cubes · Top-K = 32 KV cubes/query · H3: route 128 rows, kernel 64 rows
Partition → Coarse → Top-K → Fine → Gate
Notes: After PDD removes denoiser calls, dense attention still compares every valid token with every other valid token. For the locked 544P request, 34,373 valid packed rows imply 1,181,503,129 candidate pairs for each head in each DiT block. Video Sparse Attention first partitions the video latent into spatiotemporal cubes. In the paper default, a 4 by 4 by 4 cube represents 64 tokens. Coarse global attention scores the cubes, Top-K selection chooses the relevant regions, and fine sparse attention gathers the original K and V tokens only from selected cubes; a learned gate combines coarse and fine outputs. The paper default selects 32 KV cubes for each query cube. Keep three implementation granularities separate: the paper cube contains 64 tokens, the current H3 logical routing tile is 128 rows, and the fine kernel tile is 64 rows. VSA reduces attended token pairs and attention compute. In the current strict Ulysses route, Q, K and V are exchanged before attention and O is exchanged on the return path, so VSA alone does not automatically reduce collective payload; the learned gate adds a Q-sized forward exchange when present. VSA routing and gate weights are learned, so switching a dense checkpoint to a sparse kernel is not equivalent to a quality-qualified VSA model. The public Ref2VA PDD8 adapter and public FastH3 VSA student are separate artifacts, so this slide describes the optimization sequence rather than claiming a released combined checkpoint. The communication result is source-derived, not a measured bandwidth claim.

## Slide 10: QAD Quantizes Linears; Sage Quantizes VSA
Each path targets different SM120 kernels, and current evidence validates them separately
Path | Numerical Route | Effect | Validated Scope
QAD checkpoint | NVFP4 linears; BF16 exceptions | Recovers quantization error during distillation | 8 forwards; PDD32; VSA 90%; tile 128
Sage VSA | Q/K INT8; V FP8; BF16 output | Quantizes tile64 fine attention after routing | SM120; d=128; opt-in; Ulysses
Precision island | Token refiner: BF16; VSA default: BF16 | Keeps the sensitive short path in BF16 | Same-seed quality check pending
Inter-GPU transport | BF16 Q/K/V before Sage; BF16 O after Sage | Keeps collective payloads in BF16 | QAD and Sage do not reduce bytes
Notes: QAD is an accuracy-recovery training method: a quantized student learns under a frozen BF16 teacher. The public FastH3 Omni NVFP4-QAD artifact is an eight-forward Ref2VA checkpoint with its own PDD grid 32, 90 percent VSA and tile128 contract. The local vLLM-Omni Sage-VSA route is a separate tile64 SM120 path. It accepts BF16 tensors, quantizes Q and mean-centered K to INT8 and V to FP8 E4M3 inside the sparse fine attention kernel, and returns BF16. The token refiner stays on Torch SDPA. Ulysses exchanges Q, K and V before this local quantization and exchanges O afterward, so the current collective payload remains BF16. Do not add the public QAD artifact, Alibaba Ref2VA PDD adapter, tile64 VSA and local Sage kernel into one cumulative speedup until the exact combined path passes matched latency and quality validation.

## Slide 11: USP8 Issues Four All-to-Alls per DiT Block
Base50 runs 2,500 blocks at S = 34,432 on eight RTX PRO 5000 GPUs with local NCCL and no RDMA against a 5.167 s deadline
Scope | Tensor / Execution | A2A Rounds | Minimum Off-Rank Payload* | Rate at 5.167 s*
One DiT Block | Q / K / V forward + O reverse | 4 | 1.728 GB | 61.7 MB/rank/A2A
Base50 | 50 steps × 50 blocks = 2,500 | 10,000 | 4.319 TB | 836.0 GB/s
PDD8 | 8 steps × 50 blocks = 400 | 1,600 | 691.1 GB | 133.8 GB/s
Boundary | Current VSA / Sage keeps dense BF16 exchange | — | Logical bytes | Not achieved bandwidth
Notes: Strict Ulysses runs three forward Q, K and V all-to-alls and one reverse O all-to-all in each of 50 DiT blocks. At 50 denoiser evaluations that is 10,000 synchronized collective rounds. The 4.319 TB figure counts remote logical payload once at the sender. It excludes protocol and topology amplification and is not a wire-byte measurement. Dividing by the 5.167-second media duration gives a lower-bound payload rate, not an observed link rate. PDD8 removes the global step multiplier, but VSA and SageAttention do not automatically shrink BF16 Q, K, V and O exchange; overlap, exchanged dtype and layout, and topology-qualified RDMA must be measured separately.

## Slide 12: RDMA Precheck Passes 96/96
Q/K first
  V waits for an explicit CUDA event
Graph replay
  Fixed-address unpack remains exact after the input changes
Tiled O return
  Whole and row-chunk returns match byte for byte
Eight-GPU acceptance gate
  Full attention + W_O, end-to-end latency, memory, and Nsight overlap
Four GPUs are byte-exact; eight-GPU H3 remains pending
24 configs × 4 ranks · 8-GPU H3 candidate pending
Four-GPU Real RDMA · 96 of 96 Rank Cases Exact
Notes: The transport precheck used four physical ranks and the real RDMA route with synthetic, rank-distinct BF16 inputs. Its 96 passing rank-cases are 24 distributed configurations observed on four ranks: two row counts, three head widths, two stream priorities and two phases. It retained the production eight-slot layout, transported physical peer slots zero through three and zero-filled the other receive slots. Q and K were exchanged while V contained NaNs; only after that exchange did a producer stream publish V and record a CUDA event, which the communication stream waited on before reading V. This proves ordering and synchronization, not concurrent V projection or overlap gain. The captured graph contains only fixed-address split-QKV unpack, which remained byte-exact after inputs changed and the graph replayed. The all-RDMA collective stays outside CUDA Graph capture and explicitly refuses capture because it posts mlx5 work requests and polls completion queues from the host. Whole output return and two row-chunk returns, including the repeated coarse tail, matched independent references byte for byte. These are transport and layout exactness results; full attention, W_O, end-to-end latency, peak memory and candidate overlap were not measured. The complete eight-GPU H3 candidate therefore remains pending. Evidence bundle: real-rdma-four-gpu-20261024-v2/summary.json.

## Slide 13: Real-Time Demonstrated; Attribution Pending
Only Base50 uses the locked 960×544, 124-frame request; each optimized result uses a different workload
Status | Workload | System | Result / Limit
Measured baseline | 960×544 · 124f · 5.167 s | Base50 · BF16 · USP8 · NCCL | 247.956 s · RTF 47.992
15 s study | 960×544 · 362f · 15.083 s | PDD8 · QAD · VSA · RDMA | 14.974 s mean · RTF 0.993
10 s study | 960×544 · 243f · 10.125 s | 4-step Turbo · MXFP8 · Sage · RDMA | 6.958 s · RTF 0.687
Portrait study | 576×1024 · 119 new frames · 4.958 s | 4-step MXFP8 · Sage · FP4 VAE · RDMA | 4.459 s median · RTF 0.899
Required matched test | Lock image, audio, prompt, seed, shape, and request mode | PDD8 → VSA → QAD/Sage → RDMA | At least 3 runs per stage
Notes: Read this page as an evidence ledger, not as a performance ladder. Green means the exact locked benchmark. Blue means a result qualified inside its own study but not comparable with the green row. Orange is the acceptance work still required before we publish a cumulative optimization story.
Row A is the only current result on the locked MiniMax H3 Base Ref2VA request: 960 by 544, 124 frames at 24 FPS, 5.1667 seconds of media, the Miles reference image and voice, the locked prompt, seed 43, 50 denoising steps, BF16 dense attention, eight RTX PRO 5000 GPUs, TP1 and USP8, local NCCL, and no RDMA. After initialization and one warmup, three formal requests took 247.956, 246.201, and 248.298 seconds. The median is 247.956 seconds, or RTF 47.992. All three formal outputs and the warmup share the same MP4 SHA-256 and fully decode. The 70.84 GiB value is the maximum sampled whole-device reading across ranks over cold initialization and steady requests. It is not a PyTorch allocator high-water mark, and the ranks are materially imbalanced. Slide 6 reports the same run as 60,813 MiB steady and 72,539 MiB during cold initialization.
Row B is a different 15.083-second request: 960 by 544, 362 frames, one Zhiwei image, no external voice, an eight-forward NVFP4-QAD 36-layer decoder with VSA, and three samples per arm. Its original NCCL control averaged 17.681 seconds, while the final production arm averaged 14.974 seconds, changing RTF from 1.172 to 0.993. All three final requests met the 15.083-second media-duration budget. This is not sustained-stream evidence; the worst final request was 14.999848 seconds, only 0.152 milliseconds below a nominal 15.000-second threshold. The RDMA path also changes direct Ulysses layout handling, so its delta must not be described as isolated network transport.
Row C is internally paired but historical. Both arms use the same 960 by 544, 243-frame input and seed in that study. The original Base50 arm took 263.847 seconds; a distinct four-step Turbo, MXFP8, dense-Sage, NVFP4-VAE, TP1/SP8 and RDMA production stack took 6.958 seconds. RTF moves from 26.059 to 0.687. There is one formal sample per arm, and many material axes change together. This proves endpoint feasibility for that study, not a PDD8, VSA, QAD, Sage, or RDMA ablation.
Row D is the portrait live-avatar workload: 576 by 1024, a 124-frame request window with five-frame overlap, and therefore 119 new frames or 4.958 seconds of new media per continuation. It uses a four-step MXFP8 stack, BF16 Sage on the first sensitive attention path, NVFP4 video VAE, USP8 and RDMA. The initial request took 4.644 seconds. Five continuations have a 4.459-second median and RTF 0.899. The n label 1 + 5 means one initial request plus five continuation requests; it is not six steady samples. This is useful live-feasibility evidence, but it has no matched Base50 arm, no long-run P95, and no complete perceptual or lip-sync qualification.
The orange row is the publication gate. Keep the row-A image, audio, prompt, seed, geometry, frame count, request mode, hardware placement, timing boundary and memory method fixed. Measure Base50, PDD8, PDD8 plus VSA, the selected QAD or Sage path, and the RDMA plus overlap path with at least three steady requests per stage. Record end-to-end latency, RTF, peak GPU memory under one method, output exactness or a stated quality metric, and matched Nsight cost centers and overlap. Only then may these stages be connected as a cumulative waterfall.
The four-GPU real-RDMA precheck on the previous slide is correctness-only and is therefore absent from the performance rows. It did not run the full eight-GPU H3 model, measure end-to-end latency, or measure overlap. The 87.11 percent overlap value belongs to the separate 362-frame QAD trace and must not be attached to the Base50 row. A successful 1344 by 768 PDD8/VSA BF16 study is also component evidence only and does not fill a stage in the locked 544P chain.
Visible footer note: the 70.84 GiB value is the whole-device nvidia-smi maximum across cold and steady execution, not allocator high-water. Rows B through D are independent evidence, not a staged sequence.

## Slide 14
02 · ComfyUI Apps With vLLM-Omni
Notes: Part two focuses on ComfyUI workflows backed by vLLM-Omni multi-GPU serving, beginning with the public MiniMax H3 character-replacement work in PR #9194.

## Slide 15: vLLM-Omni Brings Multi-GPU H3 to ComfyUI
Open PR #9194 adds character replacement, continuation-aware references, and chainable LoRA controls
ComfyUI authors the workflow; vLLM-Omni runs scheduling, model execution, and multi-GPU deployment
Official vLLM-Omni Architecture
The workflow supports single- and multi-character replacement, source-derived duration, long-video continuation, and LoRA controls
ComfyUI Workflow · PR #9194
Notes: This slide opens part two. It uses the official vLLM-Omni architecture and the public PR #9194 ComfyUI character-replacement workflow. The pull request is open as of October 24, 2026.

## Slide 16
Notes: Required closing slide from NVIDIA Corporate PPT Template Starter Guide v1, page 22.